## Slide 1: Expert Opinion – Coastal flooding and adaptation
Dr Christine Lauchlan Arrowsmith
Photo credit: Water over the accessway beside the Port Fairy wharf during the June 2014 flood event (Courtesy of the Warrnambool Standard)

## Slide 2: Basis of my evidence
Streamology (2022). Tide Gauge Trigger Levels for Sea Level Rise Adaptation Pathways, Report prepared for the Glenelg Hopkins Catchment Management Authority

## Slide 3: Background
What is adaptation?
The process of adjustment to actual or expected climate and its effects to moderate harm or take advantage of beneficial opportunities.
Adaptation means adjusting decisions and activities, to manage risks and harness potential opportunities.
What are adaptation pathways?
A pathways approach maps out a range of potential adaptation options and the estimated timeline (based on best available information) for when it is likely that decisions will need to be made to guide an orderly adaptation process. This enables decision-makers to identify critical thresholds and decision points for adopting different adaptation pathway options as new information becomes available

## Slide 4: Adaptation pathways
Notes: To be adaptive to the uncertainty in the future projections of sea level rise requires the timing of any proposed action to be considered. Acting too soon can risk locking into inappropriate outcomes from economic, social, or cultural perspectives but acting too late can risk locking in considerably higher impacts later (CoastAdapt, accessed 12/10/2021). At the same time, risk management needs be able to respond effectively to new information and observed change in the physical environment (Hunter et al, 2013). This is especially so if observed change outstrips the projected rate of change compressing the timeframe over which effective action can be implemented.
A pathways approach maps out a range of potential adaptation options and the estimated timeline (based on best available information) for when it is likely that decisions will need to be made to guide an orderly adaptation process. This enables decision-makers to identify critical thresholds and decision points for adopting different adaptation pathway options as new information becomes available. Such "new information" could be realisation that the rate of sea level rise is outstripping the projected rate of change, resulting in the need to bring forward a decision point for taking an alternative pathway. If it is apparent at this future point in time that none of the pre-determined (existing) pathway options are going to be adequate, it may be necessary to identify an entirely new pathway.
It is therefore important to identify thresholds at which the adopted pathway is likely to become ineffective in meeting objectives and a new pathway for action is necessary. In other words, the approach involves establishment of a logic for anticipating what "forks in the decision-making road" might arise and what appropriate paths leading away from the fork might look like so that decisions can be made more easily. Thresholds may be related to flood protection measures like the Nominal Flood Protection Level (NFPL) used to set building floor levels or the level of service provided by assets like stormwater drains and roads. An example adaptation threshold would be an increase in mean sea level to a point where storm-tide flooding becomes too frequent for the local community to function (Stephens et al 2018); or where the NFPL applied to protect properties from a 1%AEP flood is no longer adequate because the 1%AEP flood level has increased because of sea level rise.

## Slide 5: SLR and emissions scenarios
What is the dependence of predicted sea level rise trajectories on emissions scenarios?
  An emissions pathway is the trajectory of annual greenhouse gas emissions over time
  An emissions scenario is a description of how the future may unfold.
  Future predictions of sea level rise are dependent on the assumed emissions scenario and emissions pathway adopted
Notes: Predicted sea level rise trajectories are dependent on the emissions scenario selected. However, there is considerable overlap between low and high emissions scenario trajectories to mid-century (around 2150) because of past emissions and therefore adherence to the precautionary principle in adaptation planning is warranted.
There is considerable overlap in predicted emissions scenarios till mid-century (around 2050) due to past emissions, as shown in Figure 3, which means that many of the impacts of climate change are likely to be realised despite any future emissions reductions

## Slide 6: IPCC Emissions scenarios
Emissions scenario definitions and terminology have altered over time
  Representative Concentration Pathways (RCPs) – IPCC 5th Assessment report (2014)
  Shared Socioeconomic Pathways (SSPs) – IPCC 6th Assessment report (2021)
SSP1-1.9 holds warming to approximately 1.5°C above 1850-1900 in 2100 and implies net zero CO2 emissions around the middle of the century (2050)
SSP1-2.6 stays below 2.0°C warming relative to 1850-1900 (median) with implied net zero emissions in the second half of the century (after 2050).
SSP2-4.5 scenario deviates mildly from a ‘no-additional- climate-policy’ (i.e., no new emissions reduction targets) reference scenario, resulting in a best-estimate warming around 2.7°C by the end of the 21st century relative to 1850-1900
SSP3-7.0 assumes no additional climate policy (i.e., no new emission reduction targets) and high non-CO2 emissions. This scenario assumes emissions and temperatures rise steadily and CO2 emissions roughly double from current levels by 2100.
SSP5-8.5 assumes no additional climate policy and continued socioeconomic development which includes the use of fossil fuels.
SSP5-8.5 low confidence scenario incorporates a representation of the potential effect of low-likelihood, high-impact ice sheet processes that cannot be ruled out in addition to the effects of SSP5-8.5
Notes: There have been several iterations of the IPCC emissions scenarios, although across all iterations a range of assumed future emissions assumptions from high to low ranges have been assessed. SSP5-8.5 is the high emissions scenario from the IPCC 6th Assessment report (IPCC, 2021), and it similar to the previously assessed scenarios RCP8.5 (IPCC, 2013) and A1F1 (IPCC, 2007). This scenario is a useful tool for quantifying climate risk especially over the near- to mid- term (mid-century) where many of the scenarios overlap. Schwalm et al (2020) found that "Not only are the emissions consistent with RCP8.5 in close agreement with historical total cumulative CO2 emissions (within 1%), but RCP8.5 is also the best match out to mid-century under current and stated policies with still highly plausible levels of CO2 emissions in 2100. Therefore, planning measures based around an adaptation framework accounting for SSP5-8.5 are justified.

## Slide 7: United Nations Emissions Gap Report
The latest United Nations Emissions Gap Report (UNEP, 2021) provides an overview of the difference between predicted greenhouse emissions in 2030 assuming countries are successful in implementing their climate mitigation strategies/pledges, and what these pledges actually should be to avert the worst impacts of climate change by limiting global warming to well below 2°C and pursuing no more than 1.5°C (defined as the goal of the Paris Agreement; United Nations, 2015). This difference between where we will likely be and where we need to be is referred to as the ‘emissions gap’.
The report shows that neither current policies nor the latest commitments and announced pledges across countries are consistent with limiting global warming to well below 2°C, or pursuing 1.5°C, compared to pre-industrial levels
The gap between what is required and what has been proposed is significant.
Notes: The UN Emissions Gap Report is published annually and there have been 11 previous report before the 2021 report. It is prepared by an international team of 78 leading scientists from 44 expert institutions across 24 countries, who assessed all available information, including that published in the context of the IPCC reports, as well as in other recent scientific studies. The analysis also considered the most recent mitigation pledges by different countries .
The United Nations Emissions Gap Report 2021 provides an overview of the difference between predicted greenhouse emissions in 2030 assuming countries implement their climate mitigation strategies, and what these strategies actually need to be to avert the worst impacts of climate change by limiting global warming to well below 2°C and pursuing 1.5°C (defined as the goal of the Paris Agreement; United Nations, 2015). This difference between where we will likely be and where we need to be is referred to as the ‘emissions gap’. The results of the analysis presented show that there is a significant emissions gap and that neither current policies nor the latest commitments and announced pledges by countries across the world are consistent with limiting global warming to well below 2°C, or pursuing 1.5°C, compared to pre-industrial levels. What this means is that the gap between current and future emissions rates and targets is large and therefore an increase in global mean temperature of above 2oC by 2050 will likely occur

## Slide 8: United Nations Emissions Gap Report
What the results shown in these figures mean is that the gap between current and future emissions rates and targets is large and an increase in global mean temperature of above 2oC is increasingly likely
Notes: New or updated commitments and announced pledges were shown to have only limited impact on global emissions and the emissions gap in 2030, with further reductions in emissions by 30% needed to limit warming to 2°C and 55% is needed for 1.5°C. The authors predict that if this is continued throughout this century, "it would result in warming of 2.7°C. The achievement of the net-zero pledges that an increasing number of countries are committing to would improve the situation, limiting warming to about 2.2°C by the end of the century
Figure 1 (from UNEP, 2021) provides a clear summary of the resultant global temperature increase for different emissions scenarios and the emissions gap in 2030, while Figure 2 presents the greenhouse gas emissions by country together with an indication of the level of per capita emissions consistent with 2°C and 1.5°C scenarios by 2050. The gap between what is required and what has been proposed is significant.

## Slide 9: Emissions scenarios and climate policy
2008 VCS: Based on the IPCC 4th Assessment Report (IPCC, 2007), it stated that a "policy of planning for sea level rise of not less than 0.8 metres by 2100 should be implemented" which is based on the upper bound of the projections, although not stated explicitly is aligned with the SRES A1F1 scenario (similar to RCP8.5 and SSP5-8.5).
2014 VCS:
  Plan for sea level rise of not less than 0.8 m by 2100, and allow for the combined effects of tides, storm surges, coastal processes and local conditions when assessing risks and impacts.
  Apply the precautionary principle to planning and management decision-making when considering the risks associated with climate change
2020 Victorian Marine and Coastal Strategy:
  If there are threats of serious or irreversible environmental or other damage, lack of full scientific certainty should not be used as a reason for postponing cost-effective precautionary measures to prevent environmental or other degradation
Notes: Victoria’s adoption of the RCP8.8 and now SSP8.5 scenario in Coastal Policy is a consistent position since the 2008 Victorian Coastal Strategy was released and applies the precautionary principle to planning and management decision-making when considering the risks associated with climate change. This precautionary principle has been reiterated in the Victorian Marine and Coastal Policy (2020). There are also good reasons to support increasing the sea level allowance defined in earlier VCS iterations, given increasing knowledge and understanding of factors such as compounding hazards, wave setup/runup changes and tidal amplification effects on storm surges
Recently release guidance for NZ (released August 2022, https://environment.govt.nz/assets/publications/Files/Interim-guidance-on-the-use-of-new-sea-level-rise-projections-August-2022.pdf) responds directly to the question of whether SSP5-8.5 should still be used:The upper-range scenario SSP5-8.5 (and its upper likely range of 8.5 H+) should continue to be used, given we are currently on a similar emissions trajectory, combined with the prospect of runaway polar-ice sheet instabilities and very long response time-lags (multi-decadal to centuries) in sea-level rise. This means impacts from sea-level rise will be distinctly different compared with other climate impacts that are more directly tied to global heating and therefore SSP scenarios (eg, heatwaves, precipitation, wind, etc.). These latter effects are also more responsive to cuts in global emissions and involve relatively short response times (decades), unlike sea-level rise.
.

## Slide 10: Sea level allowance
The sea level allowance was derived in the following format (Church et al, 2013):
Important assumptions:
  The variability of the storm tides will not change in time – but recent studies are identifying potential changes and we are more aware of compound hazards
  No contribution due to possible changes in wave setup or runup – but recent papers are suggesting there may future changes in wave setup
  No contribution due to changes in tides caused by sea-level rise – but in delta, estuary and coastal lagoon environments feedback or amplification of the tide can occur
  Is dependent on the distribution of uncertainty in SLR projections – High End Scenarios (HES) (e.g., those including ice melting processes) are of increasing interest
Mean sea level rise for a given scenario
Std Dev from the 5th to 95% range of projections
Scale parameter for extreme water levels

## Slide 11: Sea level allowance
Where did 0.8m SLR allowance come from?
From Hunter 2013
From Hunter 2014
Name | λ | Δz, σ | Projection | Allowance
Portland | 0.067 | 0.72, ~0.2-0.25 | 0.44, 1.22 | ~1.0 to 1.2
Based in IPCC 6th Assessment projections
Notes: In 2013 John Hunter produced a report for the Victorian Coastal Council to provide estimates of suitable sea level allowances for locations along the Victorian coast. This was based on the IPCC 4th Assessment climate scenarios. These values were slightly lower than the 0.8 applied in the VCS at that time for some locations. The he repeated the analysis in 2014 when the updated IPCC 5th Assessment RCP scenarios were release. With the new scenarios the allowance he estimated was close or above 0.8m and although he suggested the 0.8m allowance was still suitable he did note a value of 0.9 was not unreasonable.
Now the IPCC 6th Assessment SSP5-8.5 scenario has been released and I have estimated the revised allowance based on these new estimates of sea level rise. I have estimated the std deviation of the datasets and using the values for Portland estimated the revised allowance. This ranges from approx. 1.0 to 1.2 depending on the std deviation of the projections. Higher values are also possible.

## Slide 12: Local sea level rise
Notes: The Portland tide gauge is the most relevant tide gauge for monitoring sea levels for coastal communities in the Port Fairy region and is used by the BoM to provide informal and in future more formal flood watch alerts to GHCMA and Moyne Shire Council for Port Fairy and Warrnambool. Data from this tide gauge is also useful used in modelling supporting successive IPCC reports. Any local sea level projections should be added to the local mean sea level which ‘grounds’ the future sea level to a vertical datum of the locality and makes the changes relevant to the local communities. As sea level rises, the average measured mean sea level at Portland can be tracked and compared to the projections. In this way, the local change in sea level can be readily monitored and linked to predicted time frames associated with signals, triggers, and thresholds in any adaptation pathway. The data available from the Portland tide gauge clearly shows an upward trend in the rate of sea level rise, with the current rate of rise in the order of 3.4mm per year (average).

## Slide 13: Time frames
Scenario | Time when sea level rise threshold is reached (50% percentile prediction) |  |  |  |  |  | 
 | 0.2 m | 0.4 m | 0.8 m | 1.2 m | 1.6 m | 2.0 m | 2.4 m
SSP1-1.9 | 2055 | 2103 | - | - | - | - | -
SSP1-2.6 | 2052 | 2095 | - | - | - | - | -
SSP2-4.5 | 2051 | 2081 | 2135 | - | - | - | -
SSP3-7.0 | 2050 | 2073 | 2116 | 2145 | - | - | -
SSP5-8.5 | 2045 | 2066 | 2107 | 2147 | - | - | -
SSP5-8.5 (low confidence) | 2048 | 2062 | 2095 | 2121 | 2139 | - | -
Scenario | Time when sea level rise threshold is reached (95% percentile prediction) |  |  |  |  |  | 
 | 0.2 m | 0.4 m | 0.8 m | 1.2 m | 1.6 m | 2.0 m | 2.4 m
SSP1-1.9 | 2036 | 2060 | 2102 | - | - | - | -
SSP1-2.6 | 2036 | 2057 | 2092 | 2118 | - | - | -
SSP2-4.5 | 2037 | 2054 | 2086 | 2118 | 2150 | - | -
SSP3-7.0 | 2039 | 2053 | 2085 | 2105 | 2128 | - | -
SSP5-8.5 | 2033 | 2053 | 2080 | 2098 | 2117 | 2136 | -
SSP5-8.5 (low confidence) | 2030 | 2046 | 2062 | 2075 | 2085 | 2095 | 2103
Notes: Where the time to reach the sea level rise threshold is beyond 2150 the predictions have not been provided in the NASA prediction tool. This likely reflects the high level of uncertainty associated with climate modelling beyond this timeframe. Sea level rise of 2.0 m or more is only predicted before 2150 under the SSP5-8.5 at the 95th percentile and SSP5-8.5 low confidence scenarios at the 83rd percentile and above.
A key difference between these scenarios is the significantly reduced timeframes for reaching sea level rise thresholds. For example, attainment of the level of risk posed by 1.2 m increase in mean sea level could be realised 23 years earlier under the SSP5-8.5 low confidence scenario compared to the SSP5-8.5 scenario. It is also important to note that the projections for the HES (as indicated by the 95th percentile scenario results) follow similar trajectories across all the different scenarios. For example, 0.8m sea level rise is predicted to occur within a 22 year window from 2080 to 2102 (not including the low confidence scenario), with a similar range for 1.2m sea level rise (2098 to 2118).

## Slide 14: Operable lifespan of controls
The associated controls within the Port Fairy Floodplain Development Plan include the recommended minimum flood level (Nominal Flood Protection Level, NFPL) based on the 1% AEP flood level for the 1.2m mean sea level rise scenario with no added freeboard.
Analysis of levels undertaken by the CMA has shown that floors built to this level will in general, result in floor levels for new development in Port Fairy being raised in the order of 100mm above the minimum floor level the CMA is currently recommending for new development.
This level is currently the estimated 1%AEP flood level accounting for 0.8m of sea level rise, plus an added freeboard of 600mm. (Glenelg Hopkins CMA, 2021: Floor Level Analysis)
A 1.2m increase in sea level can be expected at Portland (and Port Fairy) by around 2098. At this point in time, buildings with floors finished at the 1%AEP flood level that accounts for 1.2 m sea level rise as proposed via Moyne C69 will no longer have any margin of safety above 1% AEP floods
Notes: A 1.2m increase in sea level can be expected at Portland (and Port Fairy) by around 2098 (previous slide). At this point in time, buildings with floors finished at the 1%AEP flood level that accounts for 1.2 m sea level rise as proposed via Moyne C69 will no longer have any margin of safety above 1% AEP floods. To maintain a reasonable safety margin (0.6m -which is the current minimum required at Port Fairy), it would be appropriate to begin adding a freeboard margin to this flood level estimate well prior to actual attainment of this sea level rise impact threshold. This decision point is termed a trigger point within an adaptation pathways approach.

## Slide 15: Operable lifespan of controls
Adaptation threshold (rel. sea level) | Threshold likely to be reached by (95th percentile, SSP5 8.5) | Time NFPL is effectively reduced to 0.6 m | Mean Sea Level NFPL trigger at Portland (TGZ) | Mean Sea Level NFPL trigger at Portland (m AHD)
1.2 | 2098 | 2068 | 1.17 | 0.66
This means that the best estimate of the time over which the 1.2m sea level rise flood level based NFPL is an appropriate planning control is about 36 years
Notes: Within the exhibited Port Fairy Floodplain Development Plan is included the recommended minimum flood level (Nominal Flood Protection Level, NFPL) based on the 1% AEP flood level for the 1.2m mean sea level rise scenario with no added freeboard. A 1.2m increase in sea level can be expected at Portland (and Port Fairy) by around 2098. At this point in time, buildings with floors finished at the 1%AEP flood level that accounts for 1.2 m sea level rise will no longer have any margin of safety above 1% AEP floods. To maintain a reasonable safety margin, it would be appropriate to begin adding a freeboard margin to this flood level estimate well prior to actual attainment of this sea level rise impact threshold (suggested time frame of 2058)
The projected operable lifespan of the proposed controls is around 36 years. Applying a similar logic to the previous control based on a 1% AEP storm tide with 0.8m sea level rise allowance plus 600mm freeboard the operable lifespan of the control would be around 30 years.

## Slide 16: NFPL
Which flood level estimate is appropriate for adoption as the NFPL depends on how well a flood level estimate for a future sea level rise scenario balances the burden on development in the short term, with the avoidance of impacts and damage costs in the longer term.
This approach to setting the NFPL differs from the common approach applied in the Glenelg Hopkins Region which has been to apply a minimum freeboard margin to adopted 1% AEP design flood level estimates. The difference is subtle in that a freeboard margin is built into a NFPL set using a projected (future) 1% AEP flood level estimate with no added freeboard.
The proposed NFPL is a pragmatic approach that recognises the future flood risks but doesn't impose onerous restrictions on redevelopment proposed for existing development.
Notes: NFPL is a designated level for setting the elevation of a floor level for a building so that it is provided a certain level of protection against overfloor flooding. It is based on a designated design flood (typically the 1% AEP) and an additional freeboard amount. Freeboard is a term used in the Building Act (1993). It is a factor of safety above the 1% AEP flood level, typically used in relation to the setting of floor levels to reach the NFPL. The Freeboard can account for a range of factors including wave action,
localised flow effects, uncertainties in the time-period and accuracy of the 1% AEP flood level estimate and climate change.
The proposed approach setting the NFPL by adopting the 1.2m sea level allowance with a 1% AEP storm tide and no freeboard differs from the traditional approach applied in the Glenelg Hopkins Region which has been to apply a minimum freeboard margin to adopted 1% AEP design flood level estimates. The difference is subtle in that a freeboard margin is built into a higher sea level allowance. Materially, this has limited impact on NFPLs across Port Fairy however it does increase the flood extent captured within the control. This inclusion of additional properties within the overlay provides for consideration of the uncertainty in predicting rates of sea level change and of the compounding risks associated with climate change on both coastal and catchment flooding (IPCC, 2022), follows the precautionary approach to managing the flood risk between the 0.8m and 1.2m SLR thresholds, and is consistent with an adaptation pathways approach to sea level rise flood risk management as conveyed by the Marine and Coastal Strategy

## Slide 17: NFPL
The flood extent for the higher sea level scenario is greater and therefore more properties will be subject to a flood risk consideration and the application of the NFPL within the proposed overlays, for a period potentially in the order of 36 years.
The inclusion of additional properties within the 1.2m SLR scenario flood event provides for consideration of the uncertainty in predicting rates of sea level change and of the compounding risks associated with climate change on both coastal and catchment flooding (IPCC, 2022), and follows the precautionary approach to managing the flood risk between the 0.8m and 1.2m SLR thresholds and is consistent with an adaptation pathways approach to sea level rise flood risk management as conveyed by the Marine and Coastal Strategy.
Overall, the pathway approach to the setting and revision of the NFPL applied in coastal development decisions by the CMA is valid and provides improved certainty around the requirements to management flood risk at Port Fairy through the NFPL and the time frames over which NFPLs are likely to appropriate

## Slide 18: Future NFPLs
What is certain is that sea level will continue to rise for centuries (or more), and the adequacy of NFPL conditions placed on development today will diminish into the future to the point where they are no longer adequate, so a set and forget approach to land use and development conditions is not a viable long-term option.
The CMAs proposed approach of linking future increases to the NFPL to measured changes in sea level aims to establish a clear framework for decision making that fully accounts for the wide range of plausible impact trajectories in concert with local observation of change.
Tracking annual mean sea level trend data is the main way to evaluate whether actual change is tracking within the projected range or if sea level locally is changing slower or faster than both global rates and the projected local rates
Notes: The CMAs proposed approach of linking future increases to the NFPL to measured changes in sea level aims to establish a clear framework for decision making that fully accounts for the wide range of plausible impact trajectories in concert with local observation of change. The Portland tide gauge provides a local reference for measuring actual sea level rise which can be clearly tracked against projected changes. Tracking annual mean sea level trend data is the main way to evaluate whether actual change is tracking within the projected range or if sea level locally is changing slower or faster than both global rates and the projected local rates. This aligns with Draft Marine and Coastal Strategy (DELWP, 2021) which sets out to "review the planning benchmarks for rises in sea level based on the latest and best available science (IPCC reports)" and to "establish a process for future reviews of planning benchmarks so that they are aligned with the findings of future IPCC reports and assessments

## Slide 19: IPCC 6th Assessment Report (2021)
C.2.8 Sea level rise poses a distinctive and severe adaptation challenge as it implies dealing with slow onset changes and increased frequency and magnitude of extreme sea level events which will escalate in the coming decades (high confidence). Such adaptation challenges would occur much earlier under high rates of sea level rise, in particular if low-likelihood, high impact outcomes associated with collapsing ice sheets occur (high confidence). Responses to ongoing sea level rise and land subsidence in low-lying coastal cities and settlements and small islands include protection, accommodation, advance and planned relocation (high confidence). These responses are more effective if combined and/or sequenced, planned well ahead, aligned with sociocultural values and development priorities, and underpinned by inclusive community engagement processes (high confidence).
D1.1 There is a rapidly narrowing window of opportunity to enable climate resilient development. Multiple climate resilient development pathways are still possible by which communities, the private sector, governments, nations and the world can pursue climate resilient development …... Climate resilient development pathways are progressively constrained by every increment of warming, in particular beyond 1.5°C…..
D2.1 Pathways towards climate resilient development overcome jurisdictional and organizational barriers, and are founded on societal choices that accelerate and deepen key system transitions. Planning processes and decision analysis tools can help identify low regrets options that enable mitigation and adaptation in the face of change, complexity, deep uncertainty and divergent views

## Slide 20: Sea level rise uncertainty
https://www.abc.net.au/news/2022-08-30/zombie-ice-from-greenland-will-raise-sea-level-10-inches/101384998
"That's how climate change works," Dr Colgan said. "Today's outliers become tomorrow's averages."
Greenland has lost more ice to melting than it gained from snowfall in recent years.(AP: Mstyslav Chernov)